VW-4K-2X2

API Command Set

Version: V1.0.1

# Default RS232 Settings

| Parameters | Value |
| --- | --- |
| Baud Rate | 115200 bps |
| Data bits | 8 bits |
| Parity | None |
| Stop bits | 1 bit |
| Flow control | None |

# Telnet Connection

Before you intend to control the device through telnet API, you shall establish telnet connection between this device and your computer.

The form of the command for telnet connection is below:

telnet ip (port)

ip: The device’s IP address.

port: The device’s port number, this is non-required on some Telnet control tools or platforms. Default setting is 23.

For example, if the device’s IP address is 192.168.11.143, the command for telnet connection shall be telnet 192.168.11.143

Note: Default IP setting for this device is DHCP. To obtain its IP address, please send command GET IPADDR<CR><LF> in the following command list to the device using a RS232 serial tool.

# Command Explanation

Take Command SET SW in <CR><LF> as an example:

- [SET SW] denotes command key words, case insensitive.

- [in] denotes parameters, case insensitive; incorrect parameters number will not be recognized.

- <CR><LF> denotes a carriage return or a line feed; all commands must be ended up with a carriage return or a line feed.

# Command List

| No. | Description | Command | Example |
| --- | --- | --- | --- |
| Video Mode |
| 1 | Set video mode | Command: SET VIDMODE prm <CR><LF> Return: VIDMODE prm<CR><LF> Parameter: prm = {Matrix, VideoWall, MultiView} Description: Set video output mode. | Command: SET VIDMODE Matrix<CR><LF> Return: VIDMODE Matrix<CR><LF> Description: Set video output mode. |
| 2 | Get video mode | Command: GET VIDMODE <CR><LF> Return: VIDMODE prm<CR><LF> Parameter: prm = {Matrix, VideoWall, MultiView} Description: Get video output mode. | Command: GET VIDMODE <CR><LF> Return: VIDMODE Matrix<CR><LF> Description: Get video output mode. |
| Video Wall |
| 1 | Set video wall and select input source for video wall | Command: SET VIDWALL in prm1 prm2 prm3 prm4<CR><LF> Return: VIDWALL in prm1 prm2 prm3 prm4<CR><LF> Parameter: prm1 = {out1, out2…out4}; prm2 = {out1, out2…out4}; prm3 = {out1, out2…out4}; prm4 = {out1, out2…out4}; in = {in1, in2…in4}; Description: VIDWALL is short for Video wall. Set video wall and select input source for video wall. | Command: SET VIDWALL in1 out2 out1 out3 out4<CR><LF> Return: VIDWALL in1 out2 out1 out3 out4<CR><LF> Description: Set video wall and select input source for video wall. |
| 2 | Get Video Wall settings and the input source selected | Command: GET VIDWALL<CR><LF> Return: VIDWALL in prm1 prm2 prm3 prm4<CR><LF> Parameter: prm1 = {out1, out2…out4}; prm2 = {out1, out2…out4}; prm3 = {out1, out2…out4}; prm4 = {out1, out2…out4}; in = {in1, in2…in4}; Description: VIDWALL is short for Video wall. Get Video Wall settings and the input source selected. | Command: GET VIDWALL<CR><LF> Return: VIDWALL in1 out2 out1 out3 out4<CR><LF> Description: Get Video Wall settings and the input source selected. |
| 3 | Set Video Wall bezel correction | Command: SET VIDWALLBEZEL VW OW VH OH <CR><LF> Return: VIDWALLBEZEL VW OW VH OH <CR><LF> Parameter: VW = {0-10000} OW = {0-10000} VH = {0-10000} OH = {0-10000} Description: Set Video Wall bezel correction. | Command: SET VIDWALLBEZEL 2 2 2 2 <CR><LF> Return: VIDWALLBEZEL 2 2 2 2<CR><LF> Description: Set Video Wall bezel correction. |
| 4 | Get Video Wall bezel correction | Command: GET VIDWALLBEZEL <CR><LF> Return: VIDWALLBEZEL VW OW VH OH <CR><LF> Parameter: VW = {0-10000} OW = {0-10000} VH = {0-10000} OH = {0-10000} Description: Get Video Wall bezel correction. | Command: GET VIDWALLBEZEL <CR><LF> Return: VIDWALLBEZEL 2 2 2 2<CR><LF> Description: Get Video Wall bezel correction. |
| Video Switch |
| 1 | Switch Input to Output | Command: SET SW in out<CR><LF> Return: SW in out<CR><LF> Parameter: in = {in1, in2…in4}; out = {out1, out2…out4}; Description: in -in0 means power down output SW is short for Switch Switch one input source to one output sink. | Command: SET SW in1 out2<CR><LF> Return: SW in1 out2<CR><LF> Description: Switch input 1 to hdmi output 2. |
| 2 | Switch one input for all outputs | Command: SET SW in all<CR><LF> Return: SW in all <CR><LF> Parameter: in = {in1, in2…in4}; all = {all}; Description: in - in0 means power down output SW is short for Switch Switch one input source for all output sinks. | Command: SET SW in1 all <CR><LF> Return: SW in1 all<CR><LF> Description: Switch input1 for all output sinks. |
| 3 | Get which input is mapping to the indicate Output | Command: GET MP out<CR><LF> Return: Mp in out<CR><LF> Parameter: in = {in1, in2…in4}; out = {out1, out2…out4}; Description: in - in0 means power down output MP is short for mapping Get which input is mapping to the indicate Output. | Command: GET MP out1<CR><LF> Return: MP in2 out1<CR><LF> Description: Get which input is mapping to output 1, the result is input 2. |
| 4 | Get current corresponding relationships of all inputs and all outputs | Command: GET MP all<CR><LF> Return: MP in out<CR><LF> MP in out<CR><LF> ...... Parameter: in = {in1, in2…in4}; out = {out1, out2…out4}; all = {all}; Description: in - in0 means power down output MP is short for mapping Get current corresponding relationships of all inputs and all outputs. | Command: GET MP all <CR><LF> Return: MP in1 out1<CR>... MP in2 out2<CR><LF> …... Description: Get current corresponding relationships of all inputs and all outputs. |
| Audio |
| 1 | Set Audio Mute for specific Audio Output | Command: SET AUDIO_MUTE out prm<CR><LF> Return: AUDIO_MUTE out prm<CR><LF> Parameter: out = {zone1, zone2}; prm = {on, off}; Description: Set Audio Mute for specific Audio Output. | Command: SET AUDIO_MUTE zone1 on<CR><LF> Return: AUDIO_MUTE zone1 on<CR><LF> Description: Set zone1 mute to on. |
| 2 | Get Audio Mute Status of specific Audio Output | Command: GET AUDIO_MUTE out<CR><LF> Return: AUDIO_MUTE out<CR><LF> Parameter: out = {zone1, zone2}; prm = {on, off}; Description: Get Audio Mute Status of specific Audio Output. | Command: GET AUDIO_MUTE zone1<CR><LF> Return: AUDIO_MUTE zone1 on<CR><LF> Description: Zone 1 is set to mute. |
| CEC Control |
| 1 | Set CEC POWER ON/OFF | Command: SET CEC_PWR out prm<CR><LF> Return: CEC_PWR out prm<CR><LF> Parameter: prm = {on, off} out = {out1, out2…out4, all}; Description: Set sink to power on or off. | Command: SET CEC_PWR out1 on<CR><LF> Return: CEC_PWR out1 on<CR><LF> Description: Set sink output 1 to power on. |
| 2 | Set CEC AUTO POWER ON/OFF | Command: SET AUTOCEC_FN out prm<CR><LF> Return: AUTOCEC_FN out prm<CR><LF> Parameter: prm = {on, off} out = {out1, out2…out4, all}; Description: Set sink auto power Function to ON or OFF. | Command: SET AUTOCEC_FN out1 on<CR><LF> Return: AUTOCEC_FN out1 on<CR><LF> Description: Set sink output 1 auto power function to ON. |
| 3 | Get CEC AUTO POWER ON/OFF Status | Command: GET AUTOCEC_FN out<CR><LF> Return: AUTOCEC_FN out prm<CR><LF> Parameter: prm = {on, off} out = {out1, out2…out4, all}; Description: Get Sink auto power Function ON or OFF Status. | Command: GET AUTOCEC_FN out1<CR><LF> Return: AUTOCEC_FN out1on Description: Get Sink auto power status, and the status is ON. |
| 4 | Set CEC POWER Delay Time | Command: SET AUTOCEC_D out prm<CR><LF> Return: AUTOCEC_D out prm<CR><LF> Parameter: out = {out1, out2…out4, all}; prm = {1~30}// according to the actual time counter,1 means 1 minute, 2 means 2 minutes，Default wait time is 2 minutes, Max wait time is 30 minutes. Description: AUTOCEC_D is short for CEC auto Power Delay Timing. | Command: SET AUTOCEC_D out1 2<CR><LF> Return: AUTOCEC_D out1 2<CR><LF> Description: when no active signal to hdmi1, 2 minutes later, the unit will auto power off. |
| 5 | Get CEC POWER Delay Time Status | Command: GET AUTOCEC_D out<CR><LF> Return: AUTOCEC_D out prm<CR><LF> Parameter: out = {out1, out2…out4, all}; prm = {1~30}// according to the actual time counter,1 means 1 minute, 2 means 2 minutes，Default wait time is 2 minutes, Max wait time is 30 minutes. Description: AUTOCEC_D is short for CEC auto Power Delay Timing. | Command: GET AUTOCEC_D out1<CR><LF> Return: AUTOCEC_D out1 2<CR><LF> Description: Get hdmi1 auto power delay time, the result is 2 minutes. |
| HDCP |
| 1 | Set Input HDCP support to ON/OFF | Command: SET HDCP_S in prm<CR><LF> Return: HDCP_S in prm<CR><LF> Parameter: prm = {on, off} in = {in1, in2…in4, all} Description: HDCP_S will control source hdcp support to on or off. | Command: SET HDCP_S in1 on<CR><LF> Return: HDCP_S in1 on<CR><LF> Description: Set hdmi input 1 hdcp support to on. |
| 2 | Get Input HDCP support ON/OFF Status | Command: GET HDCP_S in <CR><LF> Return: HDCP_S in prm<CR><LF> Parameter: prm = {on, off} in = {in1, in2…in4, all} Description: HDCP_S is short for HDCP support. | Command: GET HDCP_S in1<CR><LF> Return: HDCP_S in1 on<CR><LF> Description: Get hdmi1 hdcp support on or off status, and the result is on. |
| EDID |
| 1 | Set Input EDID | Command: SET EDID in prm<CR><LF> Return: EDID in prm<CR><LF> Parameter: in = {in1, in2…in4, all} prm = {1 ~16} 1: Copy form hdmi output 1 2: Copy form hdmi output 2 ... 4: Copy form hdmi output 4 5~10: Reserved 11: Fixed 4K60 2.0CH PCM Audio with HDR; 12: Fixed 4K60 2.0CH PCM Audio with SDR; 13: Fixed 4K30 2.0CH PCM Audio with HDR; 14: Fixed 4K30 2.0CH PCM Audio with SDR; 15: Fixed 1080p@60Hz 2.0CH PCM Audio with HDR; 16: Fixed 1080p@60Hz 2.0CH PCM Audio with SDR; Description: Set Input EDID. | Command: SET EDID in1 12<CR><LF> Return: EDID in1 12<CR><LF> Description: Set in1’s EDID to Fixed 4K60 2.0CH PCM Audio with SDR. |
| 2 | Get All Input EDID status | Command: GET EDID all<CR><LF> Return: EDID in prm<CR> EDID in prm<CR> EDID in prm<CR><LF> ...... Parameter: in = {in1, in2...in8}; prm = {1 ~16} 1: Copy form hdmi output 1 2: Copy form hdmi output 2 ... 4: Copy form hdmi output 4 5~10: Reserved 11: Fixed 4K60 2.0CH PCM Audio with HDR; 12: Fixed 4K60 2.0CH PCM Audio with SDR; 13: Fixed 4K30 2.0CH PCM Audio with HDR; 14: Fixed 4K30 2.0CH PCM Audio with SDR; 15: Fixed 1080p@60Hz 2.0CH PCM Audio with HDR; 16: Fixed 1080p@60Hz 2.0CH PCM Audio with SDR; Description: Get all input EDID Status. | Command: GET EDID all<CR><LF> Return: EDID in1 01<CR> EDID in2 02<CR> EDID in3 03<CR><LF> …… Description: Get all input EDID Status. |
| 3 | Get one input EDID Status | Command: GET EDID in<CR><LF> Return: EDID in prm<CR><LF> Parameter: in = {in1, in2...in4}; prm = {1 ~16} 1: Copy form hdmi output 1 2: Copy form hdmi output 2 ... 4: Copy form hdmi output 4 5~10: Reserved 11: Fixed 4K60 2.0CH PCM Audio with HDR; 12: Fixed 4K60 2.0CH PCM Audio with SDR; 13: Fixed 4K30 2.0CH PCM Audio with HDR; 14: Fixed 4K30 2.0CH PCM Audio with SDR; 15: Fixed 1080p@60Hz 2.0CH PCM Audio with HDR; 16: Fixed 1080p@60Hz 2.0CH PCM Audio with SDR; Description: Get one input EDID Status. | Command: GET EDID in1<CR><LF> Return: EDID hdmiin1 13<CR><LF> Description: Get in1 edid status, and the status is Fixed 4K30 2.0CH PCM Audio with HDR. |
| 4 | Write EDID to one input | Command: SET EDID_W in prm1 prm2<CR><LF> Return: EDID_W in prm1 prm3<CR><LF> Parameter: in = {in1, in2...in4, all}; prm1 = {block0, block1}; prm2 = one block of 256 bytes edid ascii data with spaces (hex data need conversion into ASCII code) prm3 = {ok, error}; error:check sum error Description: Write EDID content to input. | Command: SET EDID_W in1 block0 XX…XX<CR><LF> Return: EDID_W in1 block0 ok<CR><LF> Description: Write EDID content to input. |
| 5 | Read EDID of one output | Command: GET EDID_R out<CR><LF> Return: EDID_R out prm1 prm2<CR><LF> Parameter: out = {out1, out2...out4}; prm1 = {block0, block1}; prm2 = {one block of 256 bytes edid ascii data with no spaces (hex data need conversion into ASCII code), error, unconnect}; Description: Read EDID content form output. | Command: GET EDID_R out1<CR><LF> Return: EDID_R out1 block0 XX…XX<CR><LF> EDID_R out1 block1 XX…XX<CR><LF> Description: EDID_R out1 block0 XX…XX<CR><LF> --- Read EDID ok or EDID_R out1 error<CR><LF> --- Check Sum Error or EDID_R out1 unconnect<CR><LF> --- Sink unconnect |
| System Info |
| 1 | Factory reset | Command: RESET<CR><LF> Return: RESET<CR><LF> Description: Factory reset. | Command: RESET<CR><LF> Return: RESET<CR><LF> Description: Factory reset all boards. |
| 2 | System reboot | Command: REBOOT<CR><LF> Return: REBOOT<CR><LF> Description: System reboot. | Command: REBOOT<CR><LF> Return: REBOOT<CR><LF> Description: System reboot. |
| 3 | Set IR System Code | Command: Set IR_SC prm <CR><LF> Return: IR_SC prm<CR><LF> Parameter: prm = {all, mode1, mode2}; mode1 = 0x00 mode2 = 0x4e Description: Set IR System Code. | Command: Set IR_SC mode1<CR><LF> Return: IR_SC mode1<CR><LF> Description: Set IR System code to mode 1. |
| 4 | Get IR System Code | Command: Get IR_SC <CR><LF> Return: IR_SC prm<CR><LF> Parameter: prm = {all, mode1, mode2}; mode1 = 0x00 mode2 = 0x4e Description: Get IR System Code. | Command: Get IR_SC <CR><LF> Return: IR_SC mode1<CR><LF> Description: Get IR System code ，IR System code is mode 1. |
| 5 | Get the API list | Command: help<CR><LF> Return: xxxx Description: Get the API list. | Command: help<CR><LF> Return: xxxx Description: Get the API list |
| 6 | GET IP address | Command: GET IPADDR<CR><LF> Return: IPADDR xxx.xxx.xxx.xxx MASK xxx.xxx.xxx.xxx GATEWAY xxx.xxx.xxx.xxx<CR><LF> Description: GET IP address. | Command: GET IPADDR<CR><LF> Return: IPADDR 192.168.1.2 MASK 255.255.255.0 GATEWAY 192.168.2.1<CR><LF> |
| 7 | SET IP address | Command: SET IPADDR xxx.xxx.xxx.xxx MASK xxx.xxx.xxx.xxx GATEWAY xxx.xxx.xxx.xxx<CR><LF> Return: IPADDR xxx.xxx.xxx.xxx MASK xxx.xxx.xxx.xxx GATEWAY xxx.xxx.xxx.xxx<CR><LF> Description: SET IP address. | Command: SET IPADDR 192.168.1.2 MASK 255.255.255.0 GATEWAY 192.168.2.1<CR><LF> Return: IPADDR 192.168.1.2 MASK 255.255.255.0 GATEWAY 192.168.2.1<CR><LF> |
| 8 | GET Netconfig mode | Command: GET NETCFG MODE<CR><LF> Return: NETCFG MODE prm<CR><LF> Parameter: prm = {DHCP, STATIC}; Description: GET Netconfig mode. | Command: GET NETCFG MODE<CR><LF> Return: NETCFG MODE DHCP<CR><LF> |
| 9 | SET Netconfig mode | Command: SET NETCFG MODE prm<CR><LF> Return: NETCFG MODE prm<CR><LF> Parameter: prm = {DHCP, STATIC}; Description: SET Netconfig mode. | Command: SET NETCFG MODE DHCP<CR><LF> Return: NETCFG MODE DHCP<CR><LF> |
| 10 | Set the device to Standby mode | Command: STANDBY<CR><LF> Return: STANDBY!<CR><LF> | Command: STANDBY<CR><LF> Return: STANDBY!<CR><LF> |
| 11 | Wake the device | Command: WAKE<CR><LF> Return: WAKE!<CR><LF> | Command: WAKE<CR><LF> Return: WAKE!<CR><LF> |
| 12 | Get Standby | Command: GET STANDBY<CR><LF> Return: STANDBY!<CR><LF> or WAKE!<CR><LF> | Command: GET STANDBY<CR><LF> Return: STANDBY!<CR><LF> or WAKE!<CR><LF> |
| 13 | Get the connection status of the video input | Command: GET VIDIN_CONNECT in<CR><LF> Return: VIDIN_CONNECT in prm<CR><LF> in = {in1, in2...in4}; prm = {Disconnected, Connected} Description: Get the connection status of the video input. | Command: GET VIDIN_CONNECT in1<CR><LF> Return: VIDIN_CONNECT in1 Disconnected<CR><LF> |
| 14 | Get the signal status of the video input | Command: GET VIDIN_SIG in<CR><LF> Return: VIDIN_SIG in prm<CR><LF> in = {in1, in2...in4}; prm = {no, valid} Description: Get the signal status of the video input. | Command: GET VIDIN_SIG in1<CR><LF> Return: VIDIN_SIG in1 valid<CR><LF> |
| 15 | Get input video format information | Command: GET VIDIN_FORMAT in<CR><LF> Return: VIDIN_FORMAT in prm<CR><LF> in = {in1, in2...in4}; prm = { } Description: Get the resolution of the video input prm = {<horizontal>x<vertical>,<rate>; <HDR info>;<ColorSpace>,<DeepColor>} • horizontal = An integer value representing the horizontal. • vertical = An integer value representing the vertical. May have an additional qualifier such as 'i' or 'p'. • rate = An integer value representing the refresh rate. • HDR info = none hdr/ static hdr/ dynamic hdr • Color space = RGB / Ycbcr 444 /Ycbcr 422/Ycbcr 420 • DeepColor = 8 bit/10 bit /12 bit/ 16 bit | Command: GET VIDIN_FORMAT in1<CR><LF> Return: VIDIN_FORMAT in1 3840x2160,60;none hdr;rgb;8bit<CR><LF> |
| 16 | Get hdcp version of input video | Command: GET VIDIN_HDCP in<CR><LF> Return: VIDIN_HDCP in prm<CR><LF> in = {in1, in2...in4}; prm = {no hdcp, hdcp1.4, hdcp2.2} Description: Get hdcp version of input video. | Command: GET VIDIN_HDCP in1<CR><LF> Return: VIDIN_HDCP in1 no hdcp<CR><LF> |
| 17 | Get the connection status of the video output | Command: GET VIDOUT_CONNECT out<CR><LF> Return: VIDOUT_CONNECT in prm<CR><LF> out = {out1, out2...out4}; prm = {Disconnected, Connected} Description: Get the connection status of the video output. | Command: GET VIDOUT_CONNECT out1<CR><LF> Return: VIDOUT_CONNECT out1 Disconnected<CR><LF> |
| 18 | Get the signal status of the video output | Command: GET VIDOUT_SIG out<CR><LF> Return: VIDOUT_SIG out prm<CR><LF> out = {out1, out2…out4}; prm = {no, valid} Description: Get the signal status of the video output. | Command: GET VIDOUT_SIG out1<CR><LF> Return: VIDOUT_SIG out1 valid<CR><LF> |
| 19 | Get the video format information of output | Command: GET VIDOUT_FORMAT out<CR><LF> Return: VIDOUT_FORMAT out prm<CR><LF> out = {out1, out2…out4}; prm = { } Description: Get the resolution of the video input prm = {<horizontal>x<vertical>,<rate>; <HDR info>;<ColorSpace>,<DeepColor>} • horizontal = An integer value representing the horizontal. • vertical = An integer value representing the vertical. May have an additional qualifier such as 'i' or 'p'. • rate = An integer value representing the refresh rate. • HDR info = none hdr/ static hdr/ dynamic hdr • Color space = RGB / Ycbcr 444 /Ycbcr 422/Ycbcr 420 • DeepColor = 8 bit/10 bit /12 bit/ 16 bit | Command: GET VIDOUT_FORMAT out1<CR><LF> Return: VIDOUT_FORMAT out1 3840x2160,60;none hdr;rgb;8bit<CR><LF> |
| 20 | Get hdcp version of output video | Command: GET VIDOUT_HDCP out<CR><LF> Return: VIDOUT_HDCP out prm<CR><LF> out = {out1, out2…out4}; prm = {no hdcp, hdcp1.4, hdcp2.2} Description: Get hdcp version of output video. | Command: GET VIDOUT_HDCP out1<CR><LF> Return: VIDOUT_HDCP out1 no hdcp<CR><LF> |
| Update Info |
| 1 | Get selected target firmware version | Command: GET VER<CR><LF> Return: VER prm<CR><LF> Parameter: prm = {…}// according to actual firmware version Description: Get selected target firmware version. | Command: GET VER<CR><LF> Return: VER ARM VER V1.0.3 MCU VER V1.0.0 Description: Get all module firmware version. |
| 2 | Get selected target hardware version | Command: GET HW_VER<CR><LF> Return: HWVER prm<CR><LF> Parameter: prm = {…}// according to actual firmware version Description: Get selected target firmware version. | Command: GET HW_VER<CR><LF> Return: HW_VER V0.1 Description: Get all module firmware version. |
| Preset Info |
| 1 | Save Preset Scene | Command: SAVE PRESET prm<CR><LF> Return: PRESET prm<CR><LF> Parameter: prm = {1,2,3}// Description: Save Preset Scene. | Command: SAVE PRESET 1<CR><LF> Return: PRESET 1 <CR><LF> Description: Save preset scene. |
| 2 | Restore Preset Scene | Command: RESTORE PRESET prm<CR><LF> Return: PRESET prm<CR><LF> Parameter: prm = {1,2,3}// Description: Restore Preset Scene. | Command: RESTORE PRESET 1<CR><LF> Return: PRESET 1<CR><LF> Description: Restore preset scene. |
| Video Output |
| 1 | Set the scaling mode of the video output port | Command: SET VIDOUT_SCALE out prm<CR><LF> Return: VIDOUT_SCALE out prm<CR><LF> Description: out = {out1, out2…out4, all};// bypass only for out1 out2 prm = {auto, manual, bypass} § • auto -- which matches TV EDID automatically • manual --Manual change scalar output resolution • bypass -- It will bypass all HDMI source signal to sink display | Command: SET VIDOUT_SCALE out1 auto<CR><LF> Return: VIDOUT_SCALE out1 auto<CR><LF> Description: Set Scale mode to auto. |
| 2 | Get the scaling mode of the video output port | Command: GET VIDOUT_SCALE out<CR><LF> Return: VIDOUT_SCALE out prm<CR><LF> Description: out = {out1, out2…out4, all};// bypass only for out1 out2 prm = {auto, manual, bypass} | Command: GET VIDOUT_SCALE out1<CR><LF> Return: VIDOUT_SCALE out1 auto<CR><LF> Description: out1 Scale mode is auto. |
| 3 | Set output resolution | Command: SET VIDOUT_RES out prm<CR><LF> Return: VIDOUT_RES out prm<CR><LF> Description: This function can only be set in SCALE manual mode. out = {out1,out2…out4,all}; prm = { 4096x2160@60, 4096x2160@30, 4096x2160@25, 4096x2160@24, 3840x2160@60, 3840x2160@50, 3840x2160@30, 3840x2160@25, 3840x2160@24, 1920x1200@60, 1920x1080@60, 1920x1080@50, 1280x720@60, 1280x720@50, 1680x1050@60, 1600x1200@60, 1600x900@60, 1440x900@60, 1366x768@60, 1360x768@60, 1280x1024@60, 1280x960@60, 1280x800@60, 1280x768@60, 1024x768@60, 800x600@60 , } | Command: SET VIDOUT_RES out1 3840x2160@60<CR><LF> Return: VIDOUT_RES out1 3840x2160@60<CR><LF> Description: Set out1 resolution to 3840x2160@60. |
| 4 | Get output resolution | Command: GET VIDOUT_RES out<CR><LF> Return: VIDOUT_RES out prm<CR><LF> Description: out = {out1, out2…out4, all}; prm= { 4096x2160@60, 4096x2160@30, 4096x2160@25, ...... 1280x800@60, 1280x768@60, 1024x768@60, 800x600@60 } | Command: GET VIDOUT_RES out1<CR><LF> Return: VIDOUT_RES out1 4096x2160@60<CR><LF> Description: HDMI out1’s resolution is 4096x2160@60. |